## Slide 1
  Claude THERMES
  PLATEFORME DE SÉQUENÇAGE I2BC
  INSTITUT DE BILOGIE INTÉGRATIVE DE LA CELLULE
  GIF-SUR-YVETTE
  9ème ÉCOLE DE BIOINFORMATIQUE EBAII - 06/10/2020
  “LONG READS”

## Slide 2
1
2
3
Preparation of
DNA libraries
Cluster growth
Sequencing
by synthesis
General scheme of Illumina sequencing
WHY ILLUMINA READS ARE SO SHORT (≤ 300 NT) ?

## Slide 3
4-channel vs 2-channel detection
2-channel detection can cause sequencing errors due to phasing issues
and can cause polyG tracts at the end of fragments
MiSeq, HiSeq 4000 and X
MiniSeq, NextSeq, NovaSeq
SEQUENCING QUALITY

## Slide 4
Phasing/Prephasing
Percentages of bases that fell behind or jumped ahead the current cycle within a read. It increases with cycle number, hampering correct base identification for long reads. Optimal values are below 0.5 or 0.2% depending on platform. Issues may arise when read length is above specifications.
% Q-score > 30 : percentage of bases that have a a probability of incorrect base calling of 1/1000. Low Q scores can increase false-positive variant calls, which can result in inaccurate conclusions.
Q-score
Base calling error probabilities P : Q = − 10 log10 P
SEQUENCING QUALITY

## Slide 5
(acquisition of Complete Genomics in 2013)
A NEWCOMER IN SHORT READ SEQUENCING

## Slide 6
G400 NovaSeq S1 NovaSeq S4
Run time 66h 24h 48h
Output 500 Gb 500 Gb 1600-2000 Gb
Cost/Gb (€) 3.8 - 4.5 9.9 - 12.4 6.6 - 8.3
Qualité : Q30 moyen élevé (même en 2x200)
Taux d’erreur MGI < taux d’erreur NovaSeq
% reads mappés MGI > % reads mappés Illumina
Mais :
Runs plus longs (+ lavage 6h)
Preparation of nanoballs « délicate »
Régions riches A/T et G/C moins couvertes
Tests préliminaires (Genoscope, CNRGH)
NEW SEQUENCING TECHNOLOGY

## Slide 7
NGS short reads assembly
Long reads assembly
Assembly of DNA fragments with repeated sequences
Several contigs incomplete assembly, underestimation of repeats
LONG-READS VERSUS SHORT-READS

## Slide 8
Haplotype phasing
T
G
T
G
T
G
LONG-READS VERSUS SHORT-READS

## Slide 9
Detection of splicing isoforms
LONG-READS VERSUS SHORT-READS

## Slide 10
MinION - Oxford Nanopore
Single molecules
> 200 000 bp long
Error rate ≈ 10-15 %
Compensated by coverage
The 3rd generation
winning technologies
Sequel - Pacific Biosciences
Single molecules
Up to 80,000 bp long
Error rate ≈ 10-15 % - CCS: <1%
Compensated by coverage

## Slide 11
PacBio DNA-seq library
PacBio : Single Molecule Real Time (SMRT) sequencing

## Slide 12
ZMW
Pacific Biosciences

## Slide 13
Pacific Biosciences
ZMW : optical waveguide that guides light energy into a volume that is small compared to the wavelength of the light

## Slide 14
Pacific Biosciences

## Slide 15
Pacific Biosciences

## Slide 16
Pacific Biosciences

## Slide 17
Pacific Biosciences

## Slide 18
Pacific Biosciences

## Slide 21
Pacific Biosciences
Circular consensus sequencing (CCS) reads are obtained when the SMRT bell template is replicated several times by the polymerase
This allows a highly accurate sequencing by correction of random errors
Improvement with new chemistry : Circular Consensus Sequence (CCS)

## Slide 22
(Rhoads, Genomics Proteomics Bioinformatics, 2015)
2015
Half of reads > 20 kb
Top 5% of reads > 40 kb
Longest reads > 40 kb
Length of PacBio reads
Miyamoto et al. BMC Genomics (2014)
De novo assembly of Vibrio parahaemolyticus (5 Mb): two circular chromosomes
Genome assembly

## Slide 23
(Rhoads, Genomics Proteomics Bioinformatics, 2015)
Data from 35 kb size-selected E. coli library
Sequel II System ; 2.0 Chemistry
2015
Half of reads > 20 kb
Half of reads > 50 kb
2019
Top 5% of reads > 40 kb
Top 5% of reads > 135 kb
Longest reads > 40 kb
Longest reads > 175 kb
Length of PacBio reads

## Slide 24
Circular Consensus Sequences (CCS): HIFI READS

## Slide 25
Circular consensus assembly of a human genome
Wenger et al. Nat. Biotechnol. oct. 2019
Genome assembly with CCS

## Slide 26
Circular consensus assembly of a human genome
Wenger et al. Nat. Biotechnol. (2019)
Genome assembly with CCS

## Slide 27
Canu assembly
genome size > expected haploid genome because it resolves some heterozygous alleles into separate contigs
Circular consensus assembly of a human genome
Wenger et al. Nat. Biotechnol. oct. 2019
Genome assembly with CCS
  Majority of CCS read discordances
  3.4% mismatches 1 mismatch every 13,048 bp
  4.6% indels in non homopolymers. 1 non-homopolymer indel every 9,669 bp
  92.0% indels in homopolymers 1 homopolymer indel every 477 bp
  Comparison with NovaSeq
  CCS mismatch rate is 17× lower than reads from NovaSeq
  CCS indel rate is 181× higher than reads from NovaSeq
CCS reads alone : high quality contiguous genome : concordance of 99.997%

## Slide 28
Primary
tumor
Hybrid full-length transcriptome in metastatic ovarian cancer
Jing et al. Oncogene 2019
Metastases
Long-read full-length transcriptome analysis
  improves molecular diagnostic
  reveals novel therapeutic vulnerabilities
cDNA SEQUENCING

## Slide 29
from Fusberg et al. Nature Methods (2010)
Detection of 5mA with strong influence of sequence contexts: requires high coverage
Feng et al. PLOS Comput Biol (2013)
DETECTION OF MODIFIED BASES

## Slide 30
Single-molecule regulatory architectures captured by chromatin fiber sequencing Stergachis et al. Science (2020)
Detection of m6A with CCS
Fiber-seq.
DnaseI-seq.

## Slide 31
Single-molecule regulatory architectures captured by chromatin fiber sequencing Stergachis et al. Science (2020)
Detection of m6A with CCS
Notes: Representative genomic locus comparing the relationship between DNase I–seq, AdMTase-seq, and Fiber-seq at neighboring DHSs exposes the predominant all-or-none actuation of individual DHSs.

## Slide 33
  BASIC CONCEPTS
5’
DNA polymerase
or helicase ratchets
DNA through the pore
one base per step
E. Coli amyloid
secretion channel
CsgG
450 b/sec

## Slide 34
alpha-hemolysin from
Staphylococcus aureus
Porin from
Mycobacterium smegmatis
Short
sensing region
Large
sensing region
  NANOPORES USED IN THE MinION
Single nucleobase discrimination in a DNA strand
DNA sequencing
with phi29 DNA pol.
and MspA pore
E. coli assembled
de novo
MinION available
DNA transport
through alpha-hemolysin
E. Coli amyloid
secretion channel
CsgG
450 b/sec
1996
2012
2017

## Slide 35
SEQUENCING PROCESS
SEQUENCING
1D2 Library
(2017)

## Slide 36
512 X 4 pores
time
current (pA)
SEQUENCING PROCESS : MinION FLOW CELL
5-6 bases dominate the current signal
MinION : 512 pores
PromethION : 144000 pores (48 x 3000)

## Slide 37
AGGTGC
GGTGCT
GTGCTA
TGCTAT
GCTATG
CTATGT
TATGTC
time
……
….
….
….. AGGTGCTATGTCT….
5’
3’
3000 values/s
current (pA)
Basecalling : finding the optimal
path of successive 6-mers
BASECALLING
……
G A T C T G A GG A T G T C A G T G C C A T T
hexamer

## Slide 38
Size of sequenced DNA fragments
  SIZE OF SEQUENCED DNA FRAGMENTS
(Risse et al. GigaScience, 2015)
“Poor quality” profile of fragment size
10
20
0
Length of sequenced fragments (kb)
“Ultra long” reads
Size of the longest read : 778 kb
(lab.loman.net, March 2017)

## Slide 39
  SIZE OF SEQUENCED DNA FRAGMENTS

## Slide 40
  SIZE OF SEQUENCED DNA FRAGMENTS
see John Tyson’s video (ONT website)

## Slide 41
Homopolymers difficult to sequence
READ QUALITY

## Slide 42
R10
R9.4.1
“two-readers”
2019
“One-reader” pore has difficulty to read homopolymers
”Two readers” nanopore

## Slide 43
Long-read sequencing for non-small-cell lung cancer genomes
Sakamoto et al. Genome Research, Sept. 2020
GENOME SEQUENCING
Nanopore sequencing of cancer cell lines (Promethion)
Maximum length : 0.99 Mb
N50 : 32 kb
Average mapped reads : 14 kb
Biological relevance of SV further revealed by :
epigenome,
transcriptome,
protein analyses
Sequencing of clinical tumor samples
Structural aberrations also found in clinical lung adenocarcinoma specimens
Structural variants : comparison with PacBio sequencing
“These results indicated that neither the PacBio nor the PromethION platform is currently perfect; therefore, they should be used to complement each other.”

## Slide 44
GENOME SEQUENCING : TARGETED SEQUENCING
Targeted nanopore sequencing with Cas9-guided adaptor ligation
Gilpatrick et al. Nature Biotechnology April 2020
nCATS = nanopore Cas9-targeted sequencing : enrichment strategy using targeted cleavage of DNA to ligate adapters for nanopore
nCATS can simultaneously assess :
haplotype-resolved single-nucleotide variants (SNVs)
structural variations (SVs)
CpG methylation…
Best median sequencing coverage : 680 X
nCATS uses only ~3 μg of genomic DNA + can target a large number of loci in a single reaction.

## Slide 45
Detection of splice variants in surface receptor of B cells
(Byrne et al. Nat. Comm. 2017)
Library preparation
sequencing
Splice alignment uneasy due to high (5-10%) error rate
Reads are frequently truncated from 5’ end
cDNA SEQUENCING

## Slide 46
Tang et al. bioRxiv 2018
FLAIR : a pipeline for splicing isoform determination
FLAIR incorporates promoter chromatin states to distinguish 5’ truncations from true novel start sites
cDNA from chronic lymphocytic leukemia (CLL)
CHALLENGES OF NANOPORE TRANSCRIPTOME ANALYSIS

## Slide 47
THE ZIBRA PROJECT : Establishment and cryptic transmission of Zika virus in Brazil and the Americas
Mobile genomics laboratory that travelled through northeast Brazil during June 2016.
The ZiBRA laboratory screened 1,330 samples (blood) from patients in 82 municipalities across 5 federal states
The MinION protocol does not require an Internet connection for analysis, making it suitable for field applications
Viral RNA genome : + sense, 10 kb
Viral consensus sequences can be achieved in 1-2 days.
Faria et al. Nature (2017)
ZIKV was present in northeast Brazil by February 2014 and has disseminated from there, nationally and internationally.
cDNA SEQUENCING

## Slide 48
High-throughput targeted long-read single cell sequencing reveals the clonal and transcriptional landscape of lymphocytes
Singh et al., bioRxiv, 2018
RAGE-seq (Repertoire And Gene Expression sequencing) : combines targeted long-read sequencing with short-read transcriptome of barcoded single cell libraries
10x Chromium Single Cell 3’
(V2 chemistry)
Tracking of somatic mutation, alternate splicing and clonal evolution of T and B lymphocytes
BUT
Does not correct for PCR biases
T or B cell antigen receptor mRNA
NANOPORE and SINGLE CELL cDNA SEQUENCING

## Slide 49
NANOPORE and SINGLE CELL cDNA SEQUENCING
High-throughput targeted long-read single cell sequencing reveals the clonal and transcriptional landscape of lymphocytes
Lebrigand et al., Nature Communications, 2020
ScNaUmi-seq : Single-cell Nanopore sequencing with UMIs (10x Genomics Chromium system)
High accuracy cellBC and UMI assignment
Analysis of splicing and sequence variation at the single-cell level

## Slide 50
Electric signal
Canonical base distribution
DETECTION OF MODIFIED BASES

## Slide 51
Same-day genomic and epigenomic diagnosis of brain tumors (gliomas, medulloblastomas)
with nanopore sequencing
Euskirchen et al., Acta Neuropathol. (2017)
Same-day detection of :
structural variants
point mutations
methylation profiling
analysis (5-6 hours)
DETECTION OF MODIFIED BASES IN CANCER GENOMES
Single device with negligible capital cost :
outperforms hybridization-based and current sequencing technologies
makes precision medicine possible for every cancer patient

## Slide 52
sequencing
Library preparation
RNA directly sequenced in nanopore
DIRECT RNA SEQUENCING

## Slide 53
Garalde et al. Nat. Methods 2018
RNA spike in
DIRECT RNA SEQUENCING : CONTROLS

## Slide 54
Illumina Truseq
Nanopore RNA direct
(read number ; Log scale)
Sessegolo et al. Sci. Reports 2019
Illumina
Nanopore
direct RNA
DIRECT RNA SEQUENCING vs ILLUMINA

## Slide 55
For the first time a complete genome of an RNA virus sequenced in its original form
sequencing of complete genome with 100% nucleotide coverage, 99% consensus identity
Potential to identify and quantify splice variants, base modifications
not practically measurable with current methods
Direct RNA Sequencing of the complete Influenza A Virus Genome
Keller et al. Scientific Reports, Sept. 2018
Influenza A viruses are negative-sense segmented RNA viruses (8 segments)
DIRECT RNA SEQUENCING: INFLUENZA VIRUS GENOME

## Slide 56
34 genes with discordant allele specificity in two isoforms
Workman et al.Nat. Methods (2019)
Nanopore native RNA sequencing of a human transcriptome
DIRECT RNA SEQUENCING: TRANSCRIPT HAPLOTYPE

## Slide 57
Library preparation
DIRECT RNA SEQUENCING: DETECTION OF m6A
Detection of m6A with Nanopolish :
Different detection efficiency in different sites: 45% to 82%
Context dependent detection efficiency
Lorenz et al. RNA 2019

## Slide 58
DIRECT RNA SEQUENCING : detection of pseudo U
Naquin D, Gorrichon K & Costa M. I2BC Sequencing Platform 2020
pseudo U
1. In vitro synthesis of RNA molecules containing pseudo-U at fixed positions

## Slide 59
DIRECT RNA SEQUENCING : detection of pseudo U
2. Re-squiggle (Tombo)
Re-squiggle: re-segmentation of the current profile
Dwell time
Current value

## Slide 60
DIRECT RNA SEQUENCING : detection of pseudo U
Re-squiggle: re-segmentation of the current profile
2. Re-squiggle (Tombo)

## Slide 61
DIRECT RNA SEQUENCING : detection of pseudo U
3. Detection: KS statistics (Kolmogorov-Smirnov)
(Nanopolish)
Dwell time
Current value
Low detection efficiency : Sn and Sp : 30 – 50 %

## Slide 62
DIRECT RNA SEQUENCING : detection of pseudo U
pseudo U
error of base calling
psi1
psi2
psi1
psi2
Detection : strongly context dependent
Alternative strategy : detection using base calling mis-assignement
(Minimap2)

## Slide 63
Recent advances

## Slide 64
HiCanu: accurate assembly of segmental duplications, satellites, and allelic variants from high-fidelity long reads
Nurk al. Genome Research Sept. 2020
Recent advances : Assembly of PacBio HiFi reads with HiCANU

## Slide 65
Recent advances : Nanopore and 10x Genomics Visium
The spatial landscape of gene expression isoforms in tissue sections
Lebrigand et al., bioRxiv, 2020
Spatial Isoform Transcriptomics (SiT) : Genome-wide approach to explore and discover in a tissue context :
    Isoform expression (bi-allelic expression)
    Sequence heterogeneity (SNP expression)

## Slide 66
Recent advances : Illumina sequencing with Smart-seq3
Single-cell RNA counting at allele- and isoform-resolution using Smart-seq3
Hagemann-Jensenn et al. Nature Biotechnology, 2020
Count RNA molecules at allelic and transcript isoform resolution
Dimensionality reduction of 3,890 human cells colored by annotated cell type
Smart-seq3 :
full-length transcriptome coverage
5′ UMI RNA in silico reconstruction of thousands of RNA molecules/cell
60% assignments to allelic origin
30–50% assignments to specific isoforms
Smart-seq3 greatly increased sensitivity compared to Smart-seq2 detecting thousands more transcripts/cell

## Slide 67
The structure, function, and evolution of a complete human chromosome 8
Logsdon et al., bioRxiv, Sept 2020
First complete linear assembly of a human autosomal chromosome.
It resolves the sequence of five previously long-standing gaps :
2.08 Mbp centromeric α-satellite array
644 kbp defensin copy number polymorphism
863 kbp variable number tandem repeat at chromosome 8q21.2 (neocentromere)
Etc..
Barcoded Ultra-long Nanopore reads assembled into a scaffold
Regions within the scaffold with high sequence identity with PacBio HiFi contigs are replaced, thereby improving the base accuracy to >99.99%.

## Slide 68
Summary
PacBio
Maximum read length : 200 kb
CCS sequencing (HiFI reads) :
  Very low error rate, better genome assembly
  Sequencing of cDNAs (resolution of alternative splicing)
  Detection of modified DNA (6mA >> 5mC)
Nanopore
Very light sequencing system
Very long reads : maximum length >> 200 kb
Detection of modified DNA (5mC >> 6mA)
Direct sequencing of RNA :
  Direct RNA-seq
  Detection of modified RNA (6mA, pseudo U)
Illumina
Reconstruction of complete cDNAs with Smartseq3 :
  Reconstruction of thousands of RNA molecules per cell
  RNA quantification at allele and isoform resolution
PacBio
Nanopore
Illumina